## Slide 1: IOSharp: .NET Micro Framework on Linux
AUTHOR: Gerard Solé i Castellví
DIRECTOR: Juan López Rúbio
DEGREE: Bachelor in Telematics Engineering

## Slide 2: Index
1. Introduction 3
  1.1. .NET Micro Framework 4
2. IOSharp 5
  2.1. GPIO 7
  2.2. Interrupts 8
  2.3. SPI 9
  2.4. UART 10
  2.5. Example 11
3. AlterNative 12
  3.1. Translation process 13
  3.2. IOSharp C++ 15
  3.3. Example 16
4. Performance Test 17
  4.1. Example 18
5. Conclusions 19
6. Questions & Answers 22

## Slide 3: 1. Introduction
Power increase from 8 to 32 bits on microprocessors
Cost reduction on hardware production
Increasing usage of Linux in embedded devices

## Slide 4: 1. Introduction II
Cross-Platform source code generation
Performance increase on translation

## Slide 5: 1.1. .NET Micro Framework
Virtual Machine running on the bare metal
Designed for resource-constrained devices
Multiple I/O Ports and Protocols

## Slide 6: 2. IOSharp
NETMF implementation on a High-Level basis
  C# with Mono on Linux
  C library for interfacing with communication protocols
Cross-Platform  Board independent
Requires an underlying Linux
Download at
https://github.com/GerardSoleCa/IOSharp-netmf-Linux

## Slide 7: 2. IOSharp II

## Slide 8: 2.1. GPIO
Used to read or write simple High or Low States on a Pin
I/O Ports are controlled and enabled or disabled through the file system
  SYSFS  /sys/class/gpio/
  Direction
  State

## Slide 9: 2.2. Interrupts
Polling from a GPIO using the Poll function
P/Invokes are required for cross-language calls

## Slide 10: 2.3. SPI
Implemented using the provided Linux Kernel function
  Included on IOSharp-C library
  P/Invoked from C#

## Slide 11: 2.4. UART
NETMF and .NET Framework where compared
  Same namespace  System.IO.Ports
  Required methods for HomeSense in both implementations
Avoided a new reimplementation.
  IOSharp relays on Mono Serial Port (UART)

## Slide 12: 2.5. Example
Video showing HomeSense on Raspberry Pi
IOSharp requires one more transmission than NETMF in HomeSense

## Slide 13: 3. AlterNative
Source code translator written in C#
Translate a .NET Assembly to native C++
Use cases:
  Performance
  Cross-Platform development

## Slide 14: 3.1. Contributions

## Slide 15: 3.2. Translation process
void Main(string[] args){
  Console.WriteLine("Write a String"); string line = Console.ReadLine(); Console.WriteLine("Read line: " + line); byte[] b = new byte[2]; b[0] = 0; b[1] = 255; Console.WriteLine(Encoding.UTF8.GetString(b));
}
void Main(String args[]){
  Console::WriteLine(new String("Write a String")); String* line = Console::ReadLine(); Console::WriteLine(new String("Read line: ") + line); Array<char>* b = new Array<char>(2); b->SetData(0, 0); b->SetData(1, 255); Console::WriteLine(Encoding::UTF8->GetString(b));
}

## Slide 16: 3.2. Translation process II
void Main(string[] args){}
void Main(string args[]){}
Composed Identifier

## Slide 17: 3.3. IOSharp C++
IOSharp is translated using AlterNative
AlterNative System Library replaces Mono runtime

## Slide 18: 3.4. Example
AlterNative with the ILSpy interface
Translating the GPIOManager from IOSharp library

## Slide 19: 4. Performance Test
Evaluate the increased performance using AlterNative

## Slide 20: 4.1. Example
Performance test using the10K GPIO iterations

## Slide 21: 5. Conclusions
IOSharp implementation supports
  GPIO with Interrupts
  SPI
  UART
AlterNative part shows
  Improvement on IOSharp performance
  Cross-Platform with

## Slide 22: 5. Conclusions II
Future Work
    IOSharp:
      Add new protocols
      Performance optimization
    AlterNative:
      Garbage Collector
      Continuous Integration
      Extend capabilities

## Slide 23: 5. Conclusions III
Environmental Impact
    IOSharp:
      New protocols, ie.
      Performance optimization
    AlterNative:
      Garbage Collector
      Continuous Integration
      Extend C# language capabilities

## Slide 24: 6. Questions & Answers
Questions are guaranteed in life – Answers aren’t